## Slide 1: “Advances in core spectroscopy” Impurities in the core of burning plasmas: PFCs, radiation, stability, transport and diagnostic challenges
Luis F. Delgado-Aparicio et al.
Princeton Plasma Physics Laboratory (PPPL)
Princeton University, PPPL, 08/14/2018

## Slide 2: Outline
Magnetically confined fusion (MCF) plasmas and the Z-challenge
Z-studies
Radiation and the need of spectroscopy?
Novel x-ray diagnostics
Summary

## Slide 3: Tokamaks (and stellarators) around the world study different plasma parameters and shapes
DIII-D
Alcator C-Mod
LTX
NSTXU
ETE
JET
MAST
Tora
Supra
Asdex U
T10
SST-1
EAST
K-Star
JT-60SA
*Plus many
more
ITER
TCV
Pegasus
Medusa

## Slide 4: ITER will be the first time we have net energy (more energy OUT than IN)
ITER
ITER is a collaboration between USA, EU, China, Japan, Korea, India and Russia
It’s expected to produce 500MW of power using 50MW to run…this is the 1st time in history where Pout>Pin
First plasmas expected by ~ 2025
Many challenges ahead!
The Z-challenge?
(low-Z vs high-Z)

## Slide 5: The low-Z (Li, Be, C, B) vs high-Z (Fe, Mo, W) plasma facing component (PFC) challenge
Both low- & high-Z materials are currently being used for the PFCs, but each has technological hurdles.
Low-Z materials:
Typically have higher erosion rates
Their injection into the main chamber will result in an increase of Zeff and collisionality (ne,Z).
H-, D- & T-retention is a difficult issue!
Augment of Zeff will lead to:
Reduce fuel purity (nD/ne) and reactivity (Sn∝nD2 or nDnT).
But contributing less to radiated power density: Prad=nenDLD+nenCLc+SnenZLZ
NSTX-U @ PPPL, Princeton University, Princeton, NJ
MAST, CCFE,
Oxfordshire, UK
Li, B
& C

## Slide 6: The low-Z (Li, Be, C, B) vs high-Z (Fe, Mo, W) plasma facing component (PFC) challenge
Conversely, high-Z materials have good properties as a PFCs:
Low H/D/T retention.
High-heat tolerance (e.g. high melting points)
Low erosion (sputtering) rates.
Small contribution to Zeff:
Zeff=nD/ne+36nC/ne+S(nZ/ne)Z2
However, if high-Z impurities accumulate to any substantial level:
Exponentially enhance the radiation power losses (∝Z4).
Reduce the heating efficiency and modifying the overall power balance.
High-nZ/ne can lead to radiation collapse
C-Mod in Cambridge, MA, USA
EAST in China
Tore Supra/WEST in France
W
C
Mo
Mo
C
W

## Slide 7: Present and future tokamaks deal with the difficulties associated with metallic walls
Low-Z
Boron (fully stripped)
Carbon (fully stripped)
Medium-Z
Argon (He- and H-like)
High-Z
Molybdenum (Ne-like)
C-Mod (MIT), WEST (France),
JET (UK),
ASDEX (DE), EAST(China) have metallic PFCs
ITER will have Be & W PFCs
Mo & TZM
Nominal 5-7 year plan steps for implementation of high-Z wall in NSTX-U

## Slide 8: With the help of detailed simulations ITER decided on a wall with low- and high-Z PFCs
Simulations of plasma flows and plasma-wall interaction have had a decisive influence on the design of ITER wall.
Be
W
Edge localized modes (ELMs) and disruptions can impact integrity of divertor cassettes

## Slide 9: Summary 1: Its is important to understand, tailor and control Z-transport & accumulation
Understanding the sources, transport/confinement of high-Z impurities is crucial to ITER success:
- Degradation of energy confinement
- Impurity-induced macroscopic instabilities
- Fuel dilution
Controlling Z-transport to avoid accumulation in the core is necessary to achieve and maintain high fusion performance.
STUDY: - Neoclassical transport
- Turbulent-induced transport
- Effect of RMPs!
For the near future: Novel diagnostics should become an essential part of a control algorithm coupled to physics & engineer actuators for minimizing impurity accumulation in tokamaks (diagnostic development in-line with OFES mission).
Be
W

## Slide 10: Outline
Magnetically confined fusion (MCF) plasmas and the Z-challenge
Z-studies
Radiation and the need of spectroscopy?
Novel x-ray diagnostics
Summary

## Slide 11: Outline
Examples of Z-studies:
Transport & asymmetries
Core stability
Density-limit

## Slide 12: Outline
Examples of Z-studies:
Transport & asymmetries
Core stability
Density-limit

## Slide 13: Impurity transport can be complicated but now its much simpler than before (using modern diagnostics + codes)
inwards
outwards
SOURCE
Conventional transport equations (Z)
Degree of Z-peaking:
Impurity transport studies require:
Adequate radial COVERAGE (0<r/a<1)
Adequate radial and time resolution
(Dr/a~1/20, Dt~1-5 ms)
Charge-state density resolution: f(Te) (measure emissivity from several nZ’s)
Filter vs photon-energy resolution & coverage
Ability to discern between between symmetric and asymmetric phenomena: (r) vs (r,q)
Spend less time on 2D tomography and do physics!

## Slide 14: New “smart” diagnostics are needed to study impurity transport and density asymmetries
L. F. Delgado-Aparicio, et. al., RSI, 85, 11D859, (2014).
L. F. Delgado-Aparicio, et. al., to be submitted, NF, (2018).
NSTX-U
(r)
(r,q)

## Slide 15: Solutions for electrostatic potential (DF) and impurity density show in/out asymmetries
2D solution for electrostatic potential
Impurity ion density in/out asymmetries

## Slide 16: Core bremsstrahlung emission from main ion and fully stripped low-Z impurities is small

## Slide 17: Core radiation from medium- to high-Z will be affected by centrifugal forces in NSTX-U

## Slide 18: Outline
Examples of Z-studies:
Transport & asymmetries
Core stability
Density-limit

## Slide 19: Large family of macroscopic instabilities can be affected by Z-charge and radiation effects
High-Z impurities can degrade core confinement and can be the cause also of radiative density limit disruptions
Core (1/1) modes
0<r/a<0.5
Mid-radius (m/n) modes
0.3<r/a<0.9
Edge
0.9<r/a<1.1

## Slide 20: Large family of macroscopic instabilities can be affected by Z-charge and radiation effects
High-Z impurities can degrade core confinement and can be the cause also of radiative density limit disruptions
Core (1/1) modes
0<r/a<0.5
Mid-radius (m/n) modes
0.3<r/a<0.9
Edge
0.9<r/a<1.1

## Slide 21: Long-lived saturated modes are routinely observed on a number of diagnostics
Saturated mode after impurity
accumulation
Saturated mode after accumulation
+ injection
sawteeth
saturated state
LLM
Notes: SXR brightness shows initial kink-like deformation of the central plasma column

## Slide 22: Stages resemble an ideal internal kink & magnetic island produced by a resistive (1,1) mode
Co-exist with multiple sawtooth crashes
L. Delgado-Aparicio, et al., RSI’12, PRL’13, NF’13
L. Sugiyama, PoP’14

## Slide 23: …surprisingly resilient to sawtooth crashes !
tsnake~190 ms & tsawtooth~3.66 ms
⇒ ~ 20 snake periods.
Crashes may cause a transient reduction of rq=1 (dr1≲1 cm).
And a reduction of the vf
During the crash the small circular core moves rapidly outwards to the edge of the crescent radius.
Snake density is nearly untouched by thermal crash + heat pulse.

## Slide 24: Repetitive saturated modes are observed in long-pulse tokamaks with metal PFCs
Li-Qing Xu et al.
CPL’14
Challenges
Repetitive Z-modes have implications for ITER H-mode sustainability since available heating power is only slightly above the H-mode power threshold.
ITER (rq=1~a/2)
Reduce the effects on fast ions, J, q ⇒Sn, dilution, impurity peaking
Develop active control tools
MHD control (heating vs CD vs torque)
Z-control (transport vs ELMs vs 3D)
Experiments in NSTX-U/DIII-D/EAST

## Slide 25: Outline
Examples of Z-studies:
Transport & asymmetries
Core stability
Density-limit

## Slide 26: Large family of macroscopic instabilities can be affected by Z-charge and radiation effects
High-Z impurities can degrade core confinement and can be the cause also of radiative density limit disruptions
Core (1/1) modes
0<r/a<0.5
Mid-radius (m/n) modes
0.3<r/a<0.9
Edge
0.9<r/a<1.1

## Slide 27: High-Z impurity radiation can contribute cooling causing TMs to grow larger & faster
The interior region of an island contains impurities.
Island interior is shielded from any auxiliary heating being shunted around by heat conduction parallel to the B-lines.
Impurities radiate, cooling the island interior, causing it to grow faster and larger in comparison to the impurity-free cases.
Radiation (≠charge) driven islands (a.k.a. radiation-induced tearing modes: RiTMs)
MRE ⇒ onset criterion ⇒ consistent with the empirical scaling of nG=Ip/pa2
D. A. Gates and L. Delgado-Aparicio,
Phys. Rev. Letters, 108, 165004, (2012).

## Slide 28: Impurity effects & island asymmetries can be modeled using the extended MRE formalism
Symmetric island
Asymmetric island
R. White, D. A. Gates
D. P. Brennan, PoP’15
Q. Teng, D. P. Brennan,
L. Delgado-Aparicio,
D. A. Gates and J. Swerdlow, PoP’16
R. White, D. A. Gates
D. P. Brennan, PoP’15
3D resistivity with asymmetry adds destabilization term
Simple result of finite-island width in cylindrical geom.
Neither O-point or X-point are on the rational surface.
The width of the inner core-side is larger.
D. P. Brenan, D. Gates,
L. Delgado-Aparicio,
R. White, to be
submitted,
PoP ’17

## Slide 29: Impurity effects & island asymmetries can be modeled using the extended MRE formalism
3D resistivity with asymmetry adds destabilization term
Simple result of finite-island width in cylindrical geom.
Neither O-point or X-point are on the rational surface.
The width of the inner core-side is larger.
Some approximations: [(2,1) is the most unstable]
D’rs≈-m to D’rs>0 …..for m=2
D’rs≈ -2m …..for m>2
What about the growth rate C3?
If C3<0 => exponential growth => Density-limit DISRUPTION !

## Slide 30: Local onset criteria for RiTMs can be reduced to a non-dimensional form similar to nG
Where:
Onset criteria at the rational surface:
L. Delgado-Aparicio, D. A. Gates, D. P. Brennan and R. White, to be submitted to PoP, (2018)
Parameterizing
“cleanliness” ?

## Slide 31: Summary 2: Large family of macroscopic phenomena can be affected by charge & radiation
Core
(1/1)
Mid-radius
(2/1)
MHD

## Slide 32: Outline
Magnetically confined fusion (MCF) plasmas and the Z-challenge
Z-studies
Radiation and the need of spectroscopy?
Novel x-ray diagnostics
Summary

## Slide 33: Main radiation mechanisms: Bremsstrahlung (ff), radiative recombination (fb) & line-emission (bb)

## Slide 34: Radiation processes have to be calculated based on local plasma parameters [Te, ne, nZ(R,t)]
Continuum and & line emission:
Bremsstrahlung (ff):
Radiative recombination (fb):
Line emission (bb):
Visible/UV/x-ray tomography:
Emmisivity is a flux-surface function
Emmisivity is not a flux-surface function
Inversion (E=M-1xB)
0.1
10
Te [keV]
Continuum:
exp(-hn/kBTe)
Line-emission:
∝nAl
Continuum:
exp(-hn/kBTe)
∝nMo
∝nMo

## Slide 35: Radiation processes have to be calculated based on local plasma parameters [Te, ne, nZ(R,t)]
Continuum and & line emission:
Bremsstrahlung (ff):
Radiative recombination (fb):
Line emission (bb):
Visible/UV/x-ray tomography:
Emmisivity is a flux-surface function
Emmisivity is not a flux-surface function
Inversion (E=M-1xB)

## Slide 36: Coronal equilibrium (ionization balance)
Commonly used in fusion plasmas and in the solar corona
Assumes three body-recombination rate is small
Balance between electron-impact ionization and radiative recombination
Result: Ionization degree is independent of density
Charge state of ion increases with electron temperature
Low-Z ions (Be, B, C) are often fully stripped

## Slide 37: Fractional abundance calculations depend only on the local electron temperature
Fully
stripped
H-like
He-like

## Slide 38: Radiative power densities (Vis/UV/x-ray) & <Z> can be obtained using coronal equilibrium
D. E. Post, et al., Atomic Data and Nuclear Data Tables, 20, 397-439, (1977).
Parameterizing quasi-neutrality and Zeff
Radiated power density can be easily calculated using the cooling rates

## Slide 39: Radiative power densities (Vis/UV/x-ray) & <Z> can be obtained using coronal equilibrium
D. E. Post, et al., Atomic Data and Nuclear Data Tables, 20, 397-439, (1977).
Modern references for high-Z impurities include details of the electronic structure and excitation cross sections
Parameterizing equations of interest
for two-impurity plasma
L. Delgado-Aparicio, et al., to be submitted to PoP, (2018)

## Slide 40: Summary 3: Charge state of ion increases with Te and we should measure ff, fb & bb radiation
0.1
10
Te [keV]
Continuum:
exp(-hn/kBTe)
Line-emission:
∝nAr
Continuum:
exp(-hn/kBTe)
∝nMo
∝nMo
Continuum and & line emission:
Bremsstrahlung (ff)
Radiative recombination (fb)
Line emission (bb)

## Slide 41: Outline
Magnetically confined fusion (MCF) plasmas and the Z-challenge
Z-studies
Why radiation & spectroscopy?
Novel x-ray diagnostics
Summary

## Slide 42: Why is important to measure x-rays emitted from tokamak and stellarator plasmas ?
A significant fraction of the power delivered to the plasma is lost in the form of radiation [even in an ideal pure H plasma].
A subset of Prad: In real conditions could be as high as 90%.
X-rays are the most dominant source of radiation from hot plasmas: since hn~Te:
Exercise: For 100 eV<Te<20 keV ⇒ 0.5<l<130 Å⇒ X-rays!
Measurement of power losses in the x-ray range enable the characterization of parameters such as, ne, nZ, Te, Ti, vf, vq, to be used in describing/studying:
  MHD and reconection events (from hot core to cold edge).
  Transport coefficients (e.g. diffusivity and pinch velocity).
  Radial electric field (Er)
  Magnetic flux-surface reconstructions: Te(y)⇒ J and q

## Slide 43: THE X-RAY CASE: …how to diagnose x-rays from thermonuclear plasmas @ ~300million C?
Nearly 90% of the radiated power in ITER will be
in the x-ray range:
SXR: 1<E<20 keV
HXR: 20<E<400 keV

## Slide 44: Three options in the x-ray range
Conventional broadband x-ray measurements
(e.g. SXR tomography=>confinement, MHD, equilibrium).
Doppler line-radiation x-ray measurements
(e.g. nZ, Te, Ti, vf, vq, => Er).
Modern PHA & multi-energy measurements
(e.g. Zeff, nZ, Te, ne,fast).

## Slide 45: Conventional SXR tomography consists of an array of diodes integrating the local emissivity
Essential elements:
Pinhole
Thin metallic filter
SXR/Bolo detector + Amplifier + DAQ
Thick filters will help discriminate between edge and core effects.
Individual diodes or diode arrays.
Current mode: use trans-impedance amplifiers with gain of 104-107 V/A.
L. Delgado-Aparicio, et al., RSI, 81,10E303, (2010).
What happens if we don’t
use a filter?

## Slide 46: Conventional SXR tomography integrates in photon-energy using metal filter & diode arrays
MIT
PSFC
AXUV-20
AXUV-100
DIRECT
EXAMPLES
(e.g. Si)
INDIRECT
EXAMPLE
(e.g. CsITl)
Conventional tomography integrate in energy-space
CORE
EDGE
Example of spatially resolved x-ray spectra from ITER

## Slide 47: Integration means also that it is very difficult to extract local parameters from the SXR emission
MIT
PSFC
SXR tomographic systems measure the line-integrated continuum & line-emission from MCF plasmas
ne: electron density
ni: ion (H, D/T) density
nZ: impurity density (He, B, C, O, Ar, Mo, W)
Te: electron temperature
“Maxwellian” distributions f(Ee/kBTe)
q-asymmetries as F[vf: toroidal velocity, MZ: ion mass]
(vertical or tangential views are needed)
L: Length of integration, q: poloidal angle
(radial and poloidal coverage)
Tfilter(Eph): transmission function of filter
Detector response: S(Eph)
Energy
response

## Slide 48: However, conventional SXR tomography is still being used for stability, MHD & transport studies
MIT
PSFC
a) Stability and MHD [e.g. (m,n) modes and sawteeth]
b) Impurity transport (e.g. using gas injection or LBO)

## Slide 49: Three options in the x-ray range
Conventional broadband x-ray measurements
(e.g. SXR tomography=>confinement, MHD, equilibrium).
Doppler line-radiation x-ray measurements
(e.g. nZ, Te, Ti, vf, vq, => Er).
Modern PHA & multi-energy measurements
(e.g. Zeff, nZ, Te, ne,fast).
Extract local plasma information !!!

## Slide 50: How do we extract physics information from narrow and/or wider SXR energy bands ?
Narrow bands
Wider
band
Narrow energy bands
Doppler spectroscopy
High-resolution spectrometers
E/DE~10000-20000
Probes mainly the ion-channel
Ti, Vf,q, nZ
Obtain Te using line-ratio
Wider energy bands
Multi-energy spectroscopy
Low-resolution spectrometers
E/DE~10
Probes electron and ion channels
Te, nZ, DZeff, Zeff
ne,fast (e.g. LHCD, runaways)
Example of spatially resolved x-ray spectra from ITER

## Slide 51: Three options in the x-ray range
Conventional broadband x-ray measurements
(e.g. SXR tomography=>confinement, MHD, equilibrium).
Doppler line-radiation x-ray measurements
(e.g. nZ, Te, Ti, vf, vq, => Er).
Modern PHA & multi-energy measurements
(e.g. Zeff, nZ, Te, ne,fast).
Extract local plasma information !!!

## Slide 52: Motivation for developing and using new x-ray crystal imaging spectrometers
Measurement of ion-temperature (Ti), toroidal velocity (v) and impurity density (nZ) are important for understanding and optimizing confinement:
  ∇Ti driven turbulence (ITG) is a leading candidate for explaining anomalous ion thermal transport.
  b) V and dV/dr play important roles in the H-mode transition, ITB-formation, and RWM-stabilization.
  c) Z-transport/accumulation needs to be studied & controlled/avoided
Not all reactor concepts will consider NBI. Spontaneous rotation may provide the solution for stabilization.
∴ Spatially resolving x-ray crystal spectrometer enables Ti, v and nZ measurements via Doppler broadening & line shifts.

## Slide 53: Choosing the appropriate (non-perturbative) extrinsic impurity to do x-ray spectroscopy
Fractional abundance / charge state distribution
For the temperature range of interest between 0.5 and 5 keV, He and Ne are fully stripped except in the relatively cool edge region.

## Slide 54: Choosing the appropriate (non-perturbative) extrinsic impurity to do x-ray spectroscopy
For the temperature range of interest between 0.5 and 5 keV, He and Ne are fully stripped except in the relatively cool edge region.
Fractional abundance / charge state distribution
Kr or Xe could be used for diagnosing the core, but because they are more “perturbative” than Ar for the same absolute density.
Argon H- and He-like charge states are dominant between 0.5 and 5 keV

## Slide 55: X-ray crystal imaging spectrometers revolutionized our field with Ti and Vf,q profile measurements
Similar systems have been installed in NSTX, KSTAR, EAST, LHD, W7 and in the future, NSTX-U, WEST, JT60SA & ITER
H-like Ar Crystal
(sometimes replaced by He- or H-like Ca
and now by Ne-like Xe)
He-like Ar
Crystal
He-like Ar
detectors
Ne-like Mo and H-like Ar fall in the spectrum
H-like Ar detector sees also Mo-lines

## Slide 56: How crystals help us achieving high-spectral resolution (E/DE>104)
Bragg diffraction:
Assuming a constant “d”, the observed relative wavelength shift (DS: Doppler shift) is given by:
The value of Dq can be constrained by the Johann error, which is given by:
Resolving power:
For lc~5 cm (crystal length), Rc~2.7 m, q=54o, l/Dl~40000 !!!

## Slide 57: Pilatus detectors enable breakthrough of 100k pixels (min.) at single/multiple energy ranges
CMOS
readout chip
Si-sensor
2D array pn diodes
In
balls
PILATUS 100K
106 CPS/p
Operates in single photon counting mode
CMOS hybrid pixel technology
developed originally for synchrotrons
(CERN + PSI + DECTRIS)
100K to 12M pixels
(PILATUS: 172 mm, EIGER: 75 mm)
PILATUS3 900K-IPP in-vacuum detector for x-ray plasma spectroscopy
Thanks to important advances in the x-ray detector technology it is now possible to simultaneously record high resolution images of x-ray photons at single OR multiple energy ranges through direct x-ray detection.

## Slide 58: Pilatus detectors enable breakthrough of 100k pixels (min.) at single/multiple energy ranges
Operates in single photon counting mode
New maximum frame rate of 500 Hz (1ms integration + 1 ms readout).
New 107 CPS/p for PILATUS3
The comparator voltage of the readout chip (Vcmp) controls the global threshold energy.
The threshold energy can be individually refined/trimmed using a built-in 6-bits DAC (Vtrim).
digital
Photon counting circuit in each pixel
CMOS
readout chip
Si-sensor
2D array pn diodes
In
balls
PILATUS 100K
106 CPS/p
CMOS hybrid pixel technology
developed originally for synchrotrons
(CERN + PSI + DECTRIS)

## Slide 59: He-like Ar spectra is available from the cold plasma edge to the hot core
Too cold at the edge ⇒ no excitation of dielectronic satelites.
H-like Ar diffuse outward and recombine to produce the He-like ions.
Very narrow lines⇒low Ti as well.
Enough to produce the resonant-like excitation of dielectronic satellites.
Intensity of resonant w-line is f(Te).
Much wider Doppler widh⇒higher Ti

## Slide 60: Ion temperature profiles have been obtain in a variety of physics scenarios (L, H- and i-Mode)

## Slide 61: Electron temperature Te-profiles can also be obtained using line-ratios
(L. Delgado-Aparicio, un-published)
Te-measurements based on the ratio of the resonance line-w and the dielectronic satellites “n=3” and “k”
Technique applicable to Alcator C-Mod, NSTX-U, KSTAR, EAST, WEST, LHD and JT60SA.
Considered to be a secondary diagnostic technique for the electron temperature (Te) in ITER.
He-like Ar
spectra

## Slide 62: Three options in the x-ray range
Conventional broadband x-ray measurements
(e.g. SXR tomography=>confinement, MHD, equilibrium).
Doppler line-radiation x-ray measurements
(e.g. nZ, Te, Ti, vf, vq, => Er).
Modern PHA & multi-energy measurements
(e.g. Zeff, nZ, Te, ne,fast).
Extract local plasma information !!!

## Slide 63: New technology for developing multi-energy soft x-ray diagnostics is now available
0.1
10
Te [keV]
Continuum: exp(-hn/kBTe)
Continuum: exp(-hn/kBTe)
CMOS hybrid pixel technology with excellent efficiency
EXAMPLE: no line-emission
Thanks to important advances in the x-ray detector technology it is now possible to simultaneously record high resolution images of x-ray photons at single OR multiple energy ranges through direct x-ray detection.

## Slide 64: New technology for developing multi-energy soft x-ray diagnostics is now available
0.1
10
Te [keV]
CMOS hybrid pixel technology with excellent efficiency
Thanks to important advances in the x-ray detector technology it is now possible to simultaneously record high resolution images of x-ray photons at single OR multiple energy ranges through direct x-ray detection.
Continuum:
exp(-hn/kBTe)
Line-emission:
∝nSi
Continuum:
exp(-hn/kBTe)
Line-emission:
∝nAr

## Slide 65: New technology for developing multi-energy soft x-ray diagnostics is now available
Continuum:
exp(-hn/kBTe)
EXAMPLE: MOLYBDENUM
Mo-emission (Ne-, He- & H-like) between 2-5 and 17-22 keV ranges can be radially resolved
SOURCES: Mo/TZM (PFCs), Z-injector or LBO
GOALS:
Obtain nZ & DZeff by sample or bracket line-radiation
Obtain Te, Zeff, & ne,fast by sample the continuum-radiation
Line-emission:
∝nMo
Line-emission:
∝nMo
CMOS hybrid pixel technology with excellent efficiency
0.1
10
Te [keV]

## Slide 66: Motivation: Develop ME-SXR imaging for MCF plasmas with a unique capability
A unique opportunity of measuring, simultaneously, a variety of important plasma properties:
a) central electron temperature (Te,0) and profiles (Te(R,t))
b) medium- to high-Z impurity concentrations (Zeff, nZ =>DZeff)
c) the birth of suprathermal e- (ne,fast)
d) plasma position (R0, Z0)
Especially applicable for:
Spherical tokamaks: No Te ECE-measurements in STs due to low-Bf
Burning plasmas: Complement other techniques such as TS and ECE
NSTX’s 60 Hz Multi-point Thomson Scattering
Dt~16 ms
Dt~16 ms
Tore Supra fast ECE data

## Slide 67: Motivation: Develop ME-SXR imaging for MCF plasmas with a unique capability
Think large: JT60SA,
ITER & DEMO!
This technique should be explored also as a burning plasma diagnostic in-view of its simplicity and robustness.
A unique opportunity of measuring, simultaneously, a variety of important plasma properties:
a) central electron temperature (Te,0) and profiles (Te(R,t))
b) medium- to high-Z impurity concentrations (Zeff, nZ =>DZeff)
c) the birth of suprathermal e- (ne,fast)
d) plasma position (R0, Z0)
e) Te(R,Z) => Y, J & q

## Slide 68: Photon counting ME-SXR systems use Si(Li), HgI2, Si-Ge-CdTe diodes and SDDs
Detectors in photon-counting mode
(<Te>, <Zeff>, <ne,fast>, <nZ>)
    Pulse height analysis (PHA)
    Good energy resolution (100-200 eV)
    Slow time-response (20-50 ms)
    Low efficiency at high-energies
    Very poor profile definition
    Still used in our community
    (HT7, TCV, HL-2A)
K. W. Hill, et. al., RSI ’85, NF’86
Y. Shi-RSI’04, Z. Y Chen - NIMA’04, PST’05, T. Madeira-EPS’05, P. Xu-PST’09, Y. Zhang-RSI’09, A. DuBois- RSI’15
106 CPS
Amptek
Single-chord spectrometers
One spectrum per instrument
Ketek
E. H. Silver-RSI’82, J. E. Rice-PRA’82
few 104 CPS

## Slide 69: ME-SXR concepts in current mode used various filters, scintillators+PMTs, Si-diodes
L. Delgado-Aparicio, et. al., JAP’07, PPCF’07,’11, NF’09, ’11
Multi-foil arrays in current-mode
(Te and nZ profiles)
    Better profile definition:
- Line integrated measurements
- Tomographic reconstructions
- Tangential view is preferable
    Fast time-response (1 ms to 1 ms)
    Low efficiency at high-energies
    Easy to avoid low-Z emission.
    Poor energy resolution (1-5 keV)
    Still, good Te measurements!
    WARNING: Difficult to interpret in the presence of medium- to high-Z impurities (e.g. Al, Fe, Mo, W)
L. Delgado-Aparicio, et. al., RSI,’10, NF’11

## Slide 70: ME-SXR & Thomson Scattering “combo” provided fast Te(R,t) measurements in NSTX
“Fast” SXR temperature measurements done in:
Steady state in Ohmic and NBI-heated scenarios
(L. Delgado-Aparicio, et al., PPCF’07, D. J. Clayton, PPCF’13)
RF heated plasmas using HHFW waves (L. Delgado-Aparicio, et al., JAP’07)
Plasmas with slow MHD [e.g. RWMs (L. Delgado-Aparicio, et al., PPCF’10)]
2 MW
2 MW

## Slide 71: ME-SXR diode-based systems have been deployed in tokamaks and stellarators
RFX/MST-RFPs, Core
P. Franz, et al., NF’01, RSI’04, NF’13
M. McGarry, RSI’10, M. Galante, NF’15
MST
NSTX, Egde ME-SXR system
K. Tritz, et. al., RSI’12
NSTX-U, Core & Edge ME system
K. Tritz, et. al., HTPD, 2014
CTH, Core, J. L. Herfindal,
G. J. Hartwell, et al., RSI’14
TJII, Core ME-SXR system
D. Baiao, et. al., RSI’12, ‘12
EAST, Edge ME-SXR system
Y. L. Li, K. Tritz, et. al., RSI’16

## Slide 72: Pilatus detectors enable breakthrough of 100k pixels (min.) at single/multiple energy ranges
Operates in single photon counting mode
New maximum frame rate of 500 Hz (1ms integration + 1 ms readout).
New 107 CPS/p for PILATUS3
The comparator voltage of the readout chip (Vcmp) controls the global threshold energy.
The threshold energy can be individually refined/trimmed using a built-in 6-bits DAC (Vtrim).
digital
Photon counting circuit in each pixel
CMOS
readout chip
Si-sensor
2D array pn diodes
In
balls
PILATUS 100K
106 CPS/p
CMOS hybrid pixel technology
developed originally for synchrotrons
(CERN + PSI + DECTRIS)

## Slide 73: Vcomp and Vtrim allows individual coarse & fine tuning of energy range (per-pix): Ewidth~500 eV
digital
Photon counting circuit in each pixel
J. Maddox, N. Pablant,
L. Delgado-Aparicio, et al., RSI, 87, 11E320, (2016).
EW~500 eV
N. Pablant, L. Delgado-Aparicio, et al., RSI., 83, 10E526, (2012).
“Constant” width of electronic response is a great improvement over the use of filters
L. Delgado-Aparicio, et. al., RSI,’10, NF’11
Filters:

## Slide 74: New ME-SXR imaging concept combined the best features from PHA & multi-foil methods
Settings are repeated
every
2.236 mm
L. Delgado-Aparicio, et al., RSI, 87, 11E204, (2016).

## Slide 75: From sampling the continuum radiation from Ar & Mo one can measure Te & ne2Zeff
FLYCHK code, NIST
FLYCHK code, NIST

## Slide 76: Goals #1&2: TeSXR profiles can be obtained using during Ohmic, ICRH & LHCD scenarios
ICRH heats up ions & electrons.
EEDF function is still Maxwellian
Applicable to L or H-modes (including use of error fields)
LHCD drives current and heat e-
LHCD present challenges for ECE
Thin Si detectors are sensitive only to Maxwellian part of the EEDF
Ohmic

## Slide 77: Goal #3: separate dynamic evolution of Te(R,t) from transient LBO contributions during LHCD
ME-SXR inferred Te(r,t)
Estimate nZ/ne using other diagnostics and compare
Test Mo and W impurity transport in inductive & non-inductive scenarios
Tungsten density fraction
Low
SNR

## Slide 78: Summary 4: Modern diagnostics can help us resolve nZ, Te,i, Vf,q, Zeff & ne,fast profiles
CXIS
ME-SXR

## Slide 79: New core diagnostic systems will be installed in NSTX-U, MST, DIII-D, WEST, JT60SA to ITER
ITER
DEMO
JT60SA
Notes: Investigate physics which underlies the limit

## Slide 80: Summary
With the selection of W for the divertor in ITER, understanding the sources, transport and confinement of high-Z impurities is crucial to ITER success.
Avoid high-Z accumulation in the core is necessary to achieve and maintain high fusion performance in the presence of metal PFCs.
Reviewed the impact that low- to high-Z impurities have on the average plasma charge (Zeff), resistivity and radiated power density (Prad), and hence on transport, MHD instabilities and density limits.
A significant fraction of the power delivered to the plasma is lost in the form of radiation [even in an ideal pure H plasma].
In the x-ray range (subset of Prad) could be as high as 90%.
Modern diagnostics in the visible, UV and x-ray range allow us to probe nZ, Te,i, Vf,q, Zeff & ne,fast and their profiles!